|  | ¨ÉAUÀ¼ÀÆgÀÄ «zÀÄåvï ¸ÀgÀ§gÁdÄ PÀA¥À¤ ¤0iÀÄ«ÄvÀ Bangalore Electricity Supply Company Limited |  |
| --- | --- | --- |

CONVERSION OF 11KV OH LINE INTO UG AND LT OH LINE INTO UG/AB CABLE SYSTEM IN THE JURISDICTION OF BMAZ AREA, BESCOM

  - SUMMARY:

The Energy Department, Govt. of Karnataka has directed BESCOM to submit DPR for the works of Conversion of 11KV Over Head (OH) lines into UG cable system & LT OH line into UG/AB Cable system in the jurisdiction of BMAZ area under the Annual Budget programme for the Financial year 2018-19.

- NATURE OF WORKS:

- Conversion of HT Overhead lines by UG cable & providing RMUs.

- Running of New 11kV line by UG cable for bifurcation of load on the existing overloaded feeder.

- Conversion of LT Overhead lines by Under Ground (UG)/Aerial Bunched (AB) cable.

- Laying of OFC along with UG cable.

- Laying of LT UG cable & termination at Consumer premises.

- Conversion of DP/TP structure into Spun pole for erection of existing Transformers.

- Releasing of Overhead lines & DP structures.

- Returning of released materials to BESCOM stores.

- OBJECTIVES OF PROJECT:

- Improve the reliability of Power Supply – Reduction in Interruptions.

- Reduce the electrical accidents – Contact of OH Lines avoided

- Reduction in power failure – Trees/Animals coming in contact with OH line.

- Reduction in interruption - due to heavy wind, rain & storm.

- Line Clearance – Reduction in taking multiple feeders Line Clearance for safety.

- To improve the aesthetic view of Bangalore city.

- PROJECT BENEFITS:

- Better quality and reliability of power supply to consumers.

- Reduction in T & D and AT & C losses & improved load management.

- Reduction in the failure rate of distribution transformers due to LT line short circuit.

- Reduction in Unauthorized connections by tampering.

- The fatal accidents due to snapping of OH line conductors & inadequate OH line to ground clearances due to conductor sagging can be completely prevented.

- Reduction in number and duration of interruptions.

- Lower maintenance costs, smaller voltage drops and lower chances of developing faults.

Providing Optic Fibre cable for Communication System for BESCOM:

- Optical Fiber’s intrinsic EMI/RFI immunity makes it ideal for harsh electrical environments.

- Optical Fiber’s includes its easy field connector termination, easy testing with visible light, damage resistant cable, and electrical isolation.

- Greater Bandwidth & Faster Speed and Less signal degradation & Long Lifespan.

- Revenue generation - The additional Optic Fibers can be leased out to other department and agencies.

- BRIEF DETAILS ABOUT THE PROJECT:

- The Govt. of Karnataka has announced the said project during the Annual Budget programme for the Financial year 2018-19.

- The GoK has accorded approval for the said project & guaranteed for ADB Sovereign loan of Rs. 700 Crores. (100M$).

- Hon’ble KERC has accorded in-principle approval on 01.02.2019.

- During the 95th BOD meeting held on 01.03.2019 accorded approval for implementation of said project under Phase-I, II & III for an amount of Rs. 2897.49 crores.

- Central Electricity Authority (CEA) has accorded approval for said project on 08.03.2019.

- The proposal was discussed in the 92nd screening committee meeting held on 12.02.2019. Accordingly approval was accorded by MoP/GoI on 25.03.2019.

- FINANACIAL ASSISTANCE:

- BESCOM requested M/s. Asian Development Bank for financial assistance for an amount of Rs. 1330.00 Crores (Rs. 700.00Crs under Sovereign & Rs. 630.00Crores under non-sovereign loan).

- KIUDFC has accorded in principle approval for an amount of Rs. 400.00 Crores.

- BESCOM requested M/s. REC for balance amount of Rs. 2832.67 Crores.

- Remaining amount will to be borne by BESCOM from own funds.

- THE GIST OF THE PROJECT DETAILS ARE AS UNDER:

- TOTAL NO. OF SUB DIVISIONS IN BMAZ AREA	: 63 Sub Divisions

- NO. OF SUB-DIVISIONS COVERED			: 52 Sub Divisions

- TOTAL ESTIMATE COST	(Including OFC)		: Rs. 5325.22 Crores.

- PROJECT PHASES:

| Phases | No. of S/D covered | Area Covered | DPR Cost (Rs. in Crores) | Present status |
| --- | --- | --- | --- | --- |
| PHASE-I | 15 | H.S.R Layout, Indiranagar, Jeevanbheemanagar, Domlur, Peenya, Mahalakshmil Layout, Malleshwaram, Sadashivanagar, Yeshwanthapura, Rajajinagar, Vijayanagar, Nagarabhavi and Basaveshwaranagar | 1109.01 | Rate contract issued on 15.07.2019 |
| PHASE-II | 14 | Jayanagar, BTM Layout, Shiavjinagar, RR nagar, Ramamurthynagar, Yelahanka and Sahakaranagar | 1381.47 | Rate contract issued on 15.07.2019 |
| PHASE-III | 10 | ISRO layout, Banashankari IInd Stage, Chikkakallasandra, Kengeri, Ramohalli, Anjanagara, Kengeri satellite Town, Hebbala, Sanajyanagar, Ganganagar, Kaval byrasandra, Doddabidarekallu, Andrahalli, Vidyaranyapura, Thanisandra, Kothnur & Nagawara | 1351.53 | Tendering under process |
| PHASE-IV | 13 | Koramangala, Audugodi, Madiwala, Marathahalli Kundalahalli, Bommanahalli, Hongasandra, Bellandur, Panduranganagar, Thalaghattapura, Whitefield & Kadugodi, K. R Puram, mahadevapura, Hoody, Austin Town, Murgeshpalya, Jalahalli & Soldevanahalli | 1483.20 | - |
|  | 52 | GRAND TOTAL | 5325.22 |  |

PRESENT STATUS:

- Rate contracts have been issued to successful agencies for 11 Packages under PHASE-I & PHASE-II covering 29 sub divisions for an amount of         Rs. 2404.08 Crores & Survey works are under progress.

- Tenders have been invited for 10 sub divisions under PHASE-III & tendering is under process.

- For remaining 13 sub divisions will be covered under PHASE-IV.